Multiphase LBM
Ganesh Kumar B

---
Thermodynamics of two-phase flows
Free Energy
Bulk free energy should accommodate coexistence of two phases, possible for double well potential(Eg. Van der Waal, Carnahan Starling etc.,)
$$ \Psi(x) = \int [ \mathcal{F}(\rho(x)) + \mathcal{L}(\nabla\rho(x)) ] dx $$
$$ \mathcal{L}( \nabla \rho (x) ) \text { - interfacial free energy} = \frac{\kappa}{2} | \nabla \rho|^2 $$
\text{Surface Tension}
$$ \sigma = \int_{- \infty}^{\infty} \frac{\kappa}{2} | \nabla \rho|^2 $$
F_\alpha = \kappa \rho \mathbf{\nabla_{\alpha} \Delta \rho}
\text{Force from the Surface Tension}

---
Governing Equations
Continuity:
Momentum:
Force Addition:
Final Momentum Equation:
\partial_t( \rho u) + \partial_{\beta}( \rho u_{\alpha} u_{\beta} ) = -\partial_{\alpha} p + \partial_{\beta} \sigma_{\alpha \beta} + F_\alpha
\partial_t \rho + \partial_{\alpha}(\rho u_{\alpha}) = 0
\partial_t( \rho u) + \partial_{\beta}( \rho u_{\alpha} u_{\beta} ) = -\partial_{\alpha} P_{\alpha \beta} + \partial_{\beta} \sigma_{\alpha \beta}
\partial_{\alpha} p - F_{\alpha} = \partial_{\alpha}p- \kappa \rho \partial_\alpha \partial_\beta \partial_\beta \rho
= \partial_{\alpha} p - \kappa \partial_{\alpha} ( \rho \partial_{\beta} \partial_{\beta} \rho) + \kappa (\partial_{\alpha} \rho) \partial_{\beta} \partial_{\beta} \rho
= \partial_\alpha p - \kappa \partial_\alpha( \rho \partial_\beta \partial_\beta \rho) + \kappa \partial_\beta \big( (\partial_\alpha \rho) (\partial_\beta \rho) \big) - \kappa (\partial_{\beta} \rho)\partial_{\alpha} \partial_{\beta} \rho
= \partial_\beta \Big[ \left( p - \frac{\kappa}{2}(\partial_{\gamma} \rho)^2 - \kappa \rho \partial_{\gamma} \partial_{\gamma} \rho \right) \delta_{\alpha \beta} + \kappa(\partial_{\alpha} \rho)(\partial_{\beta} \rho) \Big]
\partial_{\alpha} p - F_{\alpha} = \partial_{\beta} P_{\alpha \beta}
P_{\alpha \beta} \rightarrow \text{ Korteweg's stress}

---
Chemical Potential Formulation
Momentum Equation:
Momentum Equation with Chemical potential
\mu \rightarrow \text{Chemical Potential: } \partial_{\beta} P_{\alpha \beta}= \rho \partial_{\alpha} \mu \mu = \mu^{id} + \mu^{nid}
Gibbs-Duhem Relation:
\partial_t( \rho u) + \partial_{\beta}( \rho u_{\alpha} u_{\beta} ) = -\partial_{\alpha} P_{\alpha \beta} + \partial_{\beta} \sigma_{\alpha \beta}
\partial_t( \rho u) + \partial_{\beta}( \rho u_{\alpha} u_{\beta} ) = -\rho \partial_\alpha \mu^{id} - \rho \partial_\alpha \mu^{nid} + \partial_{\beta} \sigma_{\alpha \beta}

---
Van der Waals Equation of State
Where,
;
Solving gives,
Non-Ideal Helmholtz Free Energy:
Non-Ideal Chemical Potential:
$$ \mathcal{F}^{nid} = - a \rho^2 - \rho \theta \log(1 - \rho b) $$
$$\mu^{nid} = - 2a \rho - \theta \log(1 - \rho b) + \frac{\rho b}{ 1- \rho b}\theta $$

---
Carnahan Starling
and
Where,
Solving gives,
Non-Ideal Helmholtz Free Energy:
Non-Ideal Chemical Potential:
$$p = \rho \theta \frac{1 + \eta + \eta^2 - \eta^3}{(1- \eta)^3} - a \rho^2$$
$$\eta = \frac{\rho b}{4}$$
$$\theta = \frac{k_B T}{m}$$
$$\text{At critical point } \rho_c , \theta_c: \quad \frac{\partial p}{\partial \rho} \bigg|_{\theta = \theta_c} = 0 \quad ; \quad \frac{\partial^2 p}{\partial \rho^2} \bigg|_{\theta = \theta_c} = 0
$$ a = \frac{ b \theta_c}{0.377332}$$
$$ b = \frac{0.521772}{\rho_c} $$
$$ \mathcal{F}^{nid} = - a \rho ^2 - \rho \theta \frac{3 \eta^2 - 4 \eta}{(1 - \eta)^2} $$
$$ \mu^{nid} = - 2 a \rho + \theta \frac{3 \eta^3 - 9 \eta^2 + 8 \eta}{(1 - \eta)^3}$$

---
Spurious currents
What are spurious currents?
In a quiescent drop consisting of two-phases:
Spurious Currents: non-zero velocities arising from the simulations
Reason for spurious currents:
From chemical potential External Force:
which drives the flow locally generating these currents
$$|v| = 0$$
$$F_\alpha = - \rho \partial_\alpha \mu^{nid}$$
$$\text{Discretization errors } \partial_\alpha \mu^{nid} \text{ causes force imbalance} $$

---
Chemical Potential Formulation - kappa correction
\noindent From Second Order Central Difference \begin{equation*} \tilde{\nabla}\mu_0 = \frac{\mu_0^{i+1} - \mu_0^{i-1} }{ 2\Delta x} \end{equation*} Discrete gradient of $\nabla \mu$ can be expanded \begin{align*} \tilde{\nabla}_{\alpha}\mu_0 &\approx \nabla_{\alpha} \mu_0 + \frac{\Delta x^2}{6}\nabla_\alpha \frac{d^2 \mu_0(\rho)}{dx^2} \\ & \approx \nabla_{\alpha} \mu_0 + \frac{\Delta x^2}{6}\nabla_\alpha \Big[\frac{d^2\mu_0}{d \rho^2} \Big(\frac{d \rho_0}{dx}\Big)^2 + \frac{d\mu_0}{d \rho} \frac{d^2 \rho}{dx^2} \Big] \end{align*} The term $F_\alpha$ becomes \begin{equation*} F_\alpha = \tilde{\nabla}_{\alpha}\mu_0 - \rho \frac{\Delta x^2}{6} \nabla_\alpha \Big( \frac{d^2\mu_0}{d \rho^2} \Big(\frac{d \rho}{dx}\Big)^2 \Big) - \rho \nabla_\alpha \Big( \Big( \kappa + \frac{\Delta x^2}{6} \frac{d\mu_0}{d\rho} \Big) \frac{d^2 \rho}{d x^2} \Big) \end{equation*}

---
Maxwell-Construction

---
Chemical Potential formulation - kappa correction

---
Free Energy Formulation
Helmholtz Free Energy:
This relation also holds for non-ideal part of the fluid
$$ dF = -S dT -P dv + \mu_0 dN $$
$$\text{If } \mathcal{F} = F /V \text{ is the free energy density, We have : } p = \mu_0 \rho - \mathcal{F} $$
$$ p^{nid} = \mu^{nid}_0 \rho - \mathcal{F}^{nid}$$
$$ \text{External Force Density: } g^{nid}_{\alpha} = -\partial_{\alpha} \mu^{nid}$$
$$= \partial_{\alpha}(\mu^{nid}_{0} - \kappa \nabla^2 \rho )$$
$$ = \partial_\alpha \Big{(}\frac{p^{nid} + \mathcal{F}^{nid}}{\rho} \Big{)} - \kappa \partial_\alpha(\nabla^2 \rho) $$

---
Free Energy

---
LBM Theory

---
Force Addition in LBM

---
Modification of surface tension